## Slide 1: Module 1.4 – Course Introduction
‘Jet’ Overview

## Slide 2: Jet Overview - Chassis
Jet chassis is constructed using Actobotics parts
  These are machined metal parts with various aluminum channel, hubs, wheels, and brackets
Notes: The chassis of Jet is constructed using Actobotics parts
Actobotics is a line of machine aluminum and steel components that can attach in various ways

## Slide 3: Jet Overview - Electronics
Jet electronics consist of
  NVIDIA Jetson TK1
  Arduino Mega
  Pololu H-bridge and motors
  3 sonar sensors
  GY-521 accelerometer/gyroscope
  Playstation Eye camera
  3S (11.1V) 5000mAh battery
Notes: Jet electronics consists of various electronic components that when connected are the sensing, processing, and actuating system of Jet.
The components are listed here and the next slides will go over each component in detail.

## Slide 4: Jet Overview - Software
Jet runs ROS
  ROS is the Robot Operating System which is middleware that runs on Linux
Notes: The primary software for Jet is written to utilize ROS, the robot operating system. This will be described in another lecture.

## Slide 5: Jet Overview – Architecture Diagram
Jetson TK1
Arduino
Mega
H-Bridge
Shield
Left
Motor
Right
Motor
Camera
Accel/Gyro (GY-521)
USB
USB
I2C
Sonar
Module
Sonar
Module
Sonar
Module
Encoder
readings
Notes: The Jetson TK1 is the primary controller for Jet. The TK1 runs Ubuntu Linux and ROS.
The Arduino Mega serves as the embedded controller for Jet. It reads the sensors and drives the motors. The TK1 and the Arduino Mega communicate over USB.
The H-bridge shield stacks on top of the Arduino Mega. 2 wires from each of the motors connects to the screw terminals of the H-bridge shield.
The encoder readings from each motor are sent to the Arduino Mega.
Each of the sonar modules has a 4-pin header. 2 of those 4-pins are power (5V) and ground. The other 2 pins of each header goes to the sensor shield.
The GY-521 is the accelerometer/gyroscope unit. It requires power and ground and is connect to the I2C bus on the Arduino Mega.

## Slide 6: Jet Overview – Power Supply
Jetson TK1
Arduino
Mega
H-Bridge
Shield
USB
3S (11.1V) 5000mAh Battery
Red
Power
Switch
Fuse
Notes: The battery first runs through a fuse and then runs through the red power switch.
After the power switch, the main power is split to supply power to the Jetson TK1 and to supply motor power to the H-bridge.

## Slide 7: Jet Do’s and Don’ts
Do
  Charge the battery using the correct LiPo charger and be sure Jet is turned off when charging
  When possible, turn off the TK1 first by pressing the black TK1 power button
    It may take a second before the TK1 turns off
    You can then press the red power button to turn off main power
  It is recommended to attach some bumper material to the front of Jet
Don’t
  Run the robot in a manner to stall the motors
  Run the robot at too high a speed

## Slide 8
The GPU Teaching Kit is licensed by NVIDIA and California Polytechnic State University under the Creative Commons Attribution-NonCommercial 4.0 International License.